## Slide 1
USB UART
CP2104
(USB-TO-UART BRIDGE)
Espressif
ESP32-S3-WROOM-1
USB OTG
Buttons
UDA1334A
(DAC)
PAM8403
(AMP)
Speaker out
Line out
SSD1306
(OLED Display)
MCP73831/2
(Charge Management Controller)
SCK
WS
SD
RESET
Left Channel
Right Channel
Left Channel
Right Channel
Left Speaker
Right Speaker
SCK
MISO
MOSI
RESET
Tx
Rx
D-
D+
LiPo 1S
Battery
5v
5v
I2S
I2C
GPIO

## Slide 2: Pinout
ESP32 | UDA1334A
any GPIO | 6 / SYSCLK/PLL1
any GPIO | 2 / WS
any GPIO | 3 / DATA
ESP32 | CP2104
36 / RXD0 | 20 / RXD
37 / TXD0 | 21 / TXD
ESP32 | Button / LED
any GPIO | PLAY
any GPIO | PAUSE
any GPIO | NEXT
any GPIO | PREV
any GPIO | STATUS LED
ESP32 | SDD1306
any GPIO | SDA
any GPIO | SCL
UDA1334A | PAM8403
14 / VOUTL | 7 / INL
16 / VOUTR | 10 / INR
CP2104 | USB
3 / D+ | USB D+
4 / D- | USB D-